Notes

Aircraft Performance Calculation
2019/04-19-162(I)PP

Abstract:   Lasting 10 to 15 minutes, this presentation acquaints the audience with the hazards of inaccurate and/or unreasonable aircraft performance expectations best practices associated predicting aircraft performance

Format:  Information Briefing  - Power Point presentation

Required Personnel – FAASTeam Program Manager or designated FAASTeam Rep (s)

Optional Personnel – Flight Instructors, DPEs, or others who can speak on aircraft performance prediction.

AFS 920 Support:

In addition to this guidance document, a Power Point presentation that supports the program is provided. FPMs and presenters are encouraged to customize this presentation to reflect each individual program.

Appendix I – Equipment and Staging

Equipment:

- Projection Screen & Video Projector suitable for expected audience

  - Remote computer/projector control available at lectern or presenter location

    - In lieu of remote – detail a Rep to computer/projector control.

- Presentation Computer

  - Note:  It is strongly suggested that the entire program reside on this computer.

- Back up Projector/Computer/Media as available.

- PA system suitable for expected audience

  - Microphones for Moderator and Panel

    - Optional Microphone (s) for audience

- Lectern (optional)

Staging:

- Arrange the projection screen for maximum visibility from the audience.

- Equip with PA microphones

- Place Lectern to one side of screen.  This will be used by presenters and moderator

| Slides | Script |
| --- | --- |
|  | Slide 1 2019/04-19-162(I)PP Original Author: John Steuernagle; POC Kevin Clover, AFS-850 Operations Lead, Office 562-888-2020 Presentation Note: This is the title slide for Aircraft Performance Calculation Presentation notes (stage direction and presentation suggestions) will be preceded by a Bold header: the notes themselves will be in Italic fonts. Program control instructions will be in bold fonts and look like this: (Click) for building information within a slide; or this: (Next Slide) for slide advance. Some slides may contain background information that supports the concepts presented in the program. Background information will always appear last and will be preceded by a bold Background: identification. We have included a script of suggested dialog with each slide. Presenters may read the script or modify it to suit their own presentation style. The production team hope you and your audience will enjoy the show. Break a leg! (Next Slide) |
|  | Slide 2 Presentation Note: Here’s where you can discuss venue logistics, acknowledge sponsors, and deliver other information you want your audience to know in the beginning. You can add slides after this one to fit your situation. (Next Slide) |
|  | Slide 3 In this presentation we’ll talk a little bit about aircraft performance and how faulty performance expectations have led to accidents. We’ll cite General Aviation Joint Steering Committee accident studies and safety enhancements that relate to aircraft performance. We’ll offer some human and some technology-centered performance calculation solutions And finally, we’ll give you our recommendations for increased aircraft performance awareness Presentation Note: If you’ll be discussing additional items, add them to this list (Next Slide) |
|  | Slide 4 How often have you heard these statements. You may even have said them yourself. Each of these statements relates to aircraft and pilot performance expectations. Occasionally, in the course of accident investigation, we discover that those expectations were unreasonable. In order to be confident in their performance predictions, pilots need to process some information before taking off. Some of the information is available in the POH and some is derived through calculations. (Next Slide) |
|  | Slide 5 Here we see a lot of luggage and a small plane. This pilot might find a way to get all the baggage inside the plane but can the aircraft meet his performance expectations while carrying this load? What are some of the things the pilot need to know to answer the question? (Click) Weight and balance limitations come immediately to mind. Are the takeoff weight and center of gravity within acceptable limits? Let’s face it; many pilots haven’t done a weight and balance calculation in years but, especially if you’re going to be operating near max gross weight, you’ve got to know how much your plane, fuel, passengers, and luggage weighs. (Click) This is not a good time to estimate weight. Don’t guess – weigh it. (Click) Where you distribute that weight matters. Make sure you’re well within the center of gravity envelope. Too far aft and you’re inviting a stall – too far forward and you may get a nasty surprise when you try to flare for landing. (Click) One more thing – make sure your cargo is secure. Use a cargo net, cargo straps, and seat belts to make sure your cargo stays put throughout the flight. (Next Slide) |
|  | Slide 6 Well we’ve made our weight and balance calculations and adjusted our loading to be within limits but there’s more work to be done. Before we take off we need to know what sort of performance to expect and, more importantly, what to do if we don’t get it. We’ll need to determine density altitude. That figure will be used to refine our takeoff and climb performance calculations. We’ll also have to know how much runway we have available for takeoff – and for landing if we have to return to the field. Is the runway paved, grass, gravel, or mud? Is it contaminated with snow or water. These considerations will help us to choose a normal, short-field, or soft-field takeoff configuration and technique. Once that’s decided we can get into the POH to determine how much distance will be required to takeoff and climb over any obstacles on the departure path. We’re getting close but there’s still more to be done before we launch. (Next Slide) |
|  | Slide 7 Now that we know how much runway we need it’s time to consider what will happen if we have to abort the takeoff. The 50/70 rule of thumb will be helpful here. The rule goes like this. If you haven’t attained seventy percent of your flying speed by the time you’re half way down the available runway it’s time to abort the takeoff. Whether you’re working with knots or miles per hour the math is the same. If your takeoff speed is 60 – 70 percent of that number is 42. Assuming you have 2,200 feet of runway available, you need to see 42 knots or miles per hour at the half-way point on the runway. Obviously – if you have eight to ten thousand feet of runway to work with you can delay your abort decision. (click) We should also be mindful of terrain elevation and obstructions along our departure plan. They may dictate our departure path. (click) and while we’re looking at terrain we should identify forced landing opportunities near the field. (Next Slide) |
|  | Slide 8 This topic is extremely controversial and a comprehensive discussion would take more than an hour. We’ll just cover some of the most important points here. Every year we see accidents resulting from Loss of Control after pilots decide to return to the airport in response to emergencies during takeoff or climb out. More often than not a partial or complete loss of power prompts the decision to return to the field. (click) Loss of Control accidents are usually fatal and these are no exception to the rule. That’s why it’s imperative for pilots to understand all the factors involved and commit to the appropriate course of action before the need arises. (click) The question of course is; Is it safer to land straight ahead or to return to the airport for landing. We know that, if we have three to five thousand feet of altitude to work with, returning to the airport should be no problem. We also know that there’s a number below which it’s just too dangerous to turn back. The problem is that most of us don’t know what that number is. The safe way to find your number is to work at altitude with your Flight Instructor. Simulate power loss on climb out and see how much altitude is lost in a 200 degree turn. We say 200 degrees because, if the power loss occurs while you’re on runway heading, a 180 degree likely won’t get you aligned with the runway. Do this exercise at your typical operational weight and wait approximately 3 seconds after the simulated power loss to begin maneuvering. This delay is necessary because humans typically don’t react immediately to startling events. They take a few moments to process the event before taking action. (Next Slide) |
|  | Slide 9 Having enough fuel for every flight or landing to refuel en route should be a no brainer but pilots still make off airport landings due to running out of gas. So lets consider what pilots need to know in order to predict cruise performance. We’ll need to consult the POH for power setting and fuel consumption information at our planned cruising altitude. The winds aloft forecast will give us information from which we can calculate our expected ground speed. Factor in time to climb, approach, and land plus not less than 30 minutes reserve and you’ll have a good idea of how much fuel you’ll need. Keep abreast of your fuel state while en route and be sure to check en route fuel availability before you launch. (Next Slide) |
|  | Slide 10 By the way – unless they’re reading empty, aircraft fuel gauges give at best, an approximation of how much fuel you have on board. Fuel flow computers give a much better picture but most require pilots to input fuel quantity so starting with the right fuel state is paramount. Regardless of how you’re equipped, It’s a good practice to double check fuel quantity when you’re launching with less than full tanks. (Next Slide) |
|  | Slide 11 Here are some gold seal best practices that are recommended for all pilots (Click) It’s essential to keep track of your available fuel. Hourly – or whenever you switch tanks – calculate how long you can fly with your remaining fuel. Compare that to your predicted time to destination. If it looks as if you’re going to dip into your fuel reserve, it’s time to plan an en route fuel stop. (Click) Don’t wait till your close to your destination to refuel. The closer you get – the more you’ll be tempted to continue on your reserve fuel supply. (Click) Many pilots plan their flights so that they never land with less than one hours’ fuel in their tanks. That way they know they always meet VFR fuel reserve requirements. Whether or not this practice meets IFR reserve requirements depends on how far it is to your alternate airport. (Next Slide) |
|  | Slide 12 Briefing each and every takeoff, approach, and landing is another gold seal best practice. Vocalizing important points and procedures just before takeoff or landing keeps them uppermost in your mind where they’re available for ready reference if something unforeseen happens. (Click) Brief the assigned runway and available distance for takeoff or landing. Include aircraft configuration and target airspeeds. Vocalize your rejected takeoff or go-around decision point. Include the departure or approach path and the altitude below which you’ll not attempt a return to the airport. Finally, brief forced landing opportunities close to the airport. (Next Slide) |
|  | Slide 13 Presentation Note: You may wish to provide your contact information and main FSDO phone number here. Modify with your information or leave blank. (Next Slide) |
|  | Slide 14 Have you earned your WINGS? Proficiency is key to success in almost every thing worth doing – especially flying. Proficient pilots are confident, capable, and safe. WINGS is a proficiency training system specifically designed for general aviation pilots and, regular participation will keep you on top of your flying game. (Next Slide) |
|  | Slide 15 Now there’s even more reasons to participate in WINGS. Every time you complete a WINGS Phase you’re eligible to win cash the WINGS Sweepstakes. The sweepstakes is generously funded by Paul Burger, a long time advocate for general aviation safety and a retired aviator who believes participation in this program saves lives. VISIT WWW.MYWINGSINIATIVE.ORG to learn more and enter the sweepstakes. (Next Slide) |
|  | Slide 16 After you’ve completed a phase of WINGS you can enter the sweepstakes by clicking on “Claim Rewards” in the “WINGS – at a glance” section of your My WINGS page and select WINGS Sweepstakes. Or you can go directly to the mywingsinitiative.org website. (Next Slide) |
|  | Slide 17 Your presence here shows that you are vital members of our General Aviation Safety Community. The high standards you keep and the examples you set are a great credit to you and to GA. Thank you for attending. (Next Slide) |
|  | Slide 18 (The End) |