## Slide 1: The National FAA Safety Team Presents
Topic of the Month November
Controlled Flight Into Terrain (CFIT)
<Audience>
<Presenter>
< >
Notes: 2018/4-5-124 (I) PP Original Author: J. Steuernagle March 2017 POC: K. Clover, AFS-920 Operations Lead Office 562-888-2020
Presentation Note: This is the title slide for Controlled Flight Into Terrain (CFIT)
Presentation notes (stage direction and presentation suggestions) will be preceded by a Bold header: the notes themselves will be in Italic fonts.
Program control instructions will be in bold fonts and look like this: (Click) for building information within a slide; or this: (Next Slide) for slide advance.
Some slides may contain background information that supports the concepts presented in the program.
Background information will always appear last and will be preceded by a bold Background: identification.
We have included a script of suggested dialog with each slide. Presenters may read the script or modify it to suit their own presentation style.
The production team hope you and your audience will enjoy the show. Break a leg!
(Next Slide)

## Slide 2: Welcome
Exits
Restrooms
Emergency Evacuation
Breaks
Sponsor Acknowledgment
Set phones & pagers to silent or off
Other information
Notes: Presentation Note: Here’s where you can discuss venue logistics, acknowledge sponsors, and deliver other information you want your audience to know in the beginning.
You can add slides after this one to fit your situation. (Next Slide)

## Slide 3: Overview
The CFIT Accident
SRM solutions and GAJSC safety enhancements
Technology Solutions
Tips and Tricks
GAJSC – General Aviation Joint Steering Committee
Notes: In this presentation we’ll talk a little bit about Controlled Flight Into Terrain (CFIT) Accidents and recommendations (termed safety enhancements) from the General Aviation Joint Steering Committee - a work group that studies General Aviation Accidents. We’ll discuss some Safety Risk Management and Technological solutions to CFIT challenges and, finally; we’ll give you some tips and tricks that will help you to avoid CFIT accidents.
Presentation Note: If you’ll be discussing additional items, add them to this list
(Next Slide)

## Slide 4: The CFIT Accident
Unintentional Collision with Terrain while an Aircraft is Under Positive Control
In one year
  41 CFIT Accidents
    56% Fatal
  Inexperienced Pilots
  Dark Night and/or IMC
Flight Environment
Notes: CFIT is defined as an unintentional collision with terrain while an aircraft is under positive control.
For this presentation we looked at a typical year in which we see about forty CFIT Accidents at least half of which are fatal. (Click)
It’s logical to think that CFIT accidents usually involve inexperienced pilots in dark night and/or instrument meteorological conditions. (Click)
In fact, in a typical year more than 75 percent of CFIT accidents occur in daylight and more than half of those are in visual conditions.
(Next Slide)

## Slide 5: The CFIT Accident
Pilot Certificate Level
Instrument Rating
Notes: As we might expect – the majority of CFIT pilots hold Private certificates but Commercial and ATP pilots and flight instructors are well represented too.
You might think that most CFIT Pilots are not instrument rated and that’s correct. (Click)
But in a typical year, more than a third of CFIT pilots hold instrument ratings.
(Next Slide)

## Slide 6: The CFIT Accident
Continued VFR into IMC
  Accidents are almost always fatal
  11 Accidents in study group
    25% of total
    6 Pilots were instrument rated
    5 were not instrument rated
Notes: Continued VFR into IMC is the deadliest accident precursor. We don’t know how often pilots are successful in pursuing the impossible dream. Undoubtedly some get away safely but continued VFR into IMC accidents are usually fatal. (Click)
Of the 41 accidents in our study group, 11 – or 25% of the total – were preceded by Continued VFR into IMC and they were all fatal. You’d think that VFR pilots would more often be involved in Continued VFR accidents but they were evenly split in this study group.
(Next Slide)

## Slide 7: The CFIT Accident
IFR Procedural Mistakes
  Flight below minimum en route or crossing altitudes
  Descent below MDA
  Failure to fly assigned heading or altitude
Wire Strikes
  Common in – but not exclusive to - Ag Operations
  Most are below 200 Ft. AGL
  Many wires are unmarked
Notes: IFR procedural mistakes account for a significant portion of CFIT accidents each year. Instrument pilots must be sure they’re complying with all aspects of the clearances they accept and the procedures they fly. (Click)
Wire Strikes are often cited in CFIT accident reports and they are common in Agricultural Operations but more than half of them are not associated with Ag flying. It’s true that there are some very high towers around and their support wires can extend well beyond the tower itself. But there are relatively few collisions with tall towers or their support structures. (Click)
In fact, most wire strikes occur below 200 feet AGL. You’ve got to wonder; what required the pilots to be that low – especially in the vicinity of wires? (Click)
And be aware that many wires are unmarked. Give yourself some room. A little extra altitude – even 500 feet – will keep you above 90% of the wires.
(Next Slide)

## Slide 8: The CFIT Accident
Unrealistic aircraft performance expectations
  Density Altitude
  Short and/or obstructed runways
  Weight and balance
  Carb ice
  Tailwinds
Notes: Some CFIT accidents are caused by unrealistic expectations for aircraft performance. High Density Altitude combined with a short and/or obstructed runway and aircraft at near gross weight have resulted in collisions with obstacles on take off. Carburetor or induction system ice can reduce climb performance with the same result. And tailwinds on approach or takeoff can precede CFIT.
(Next Slide)

## Slide 9: The CFIT Accident
Incapacitation
  1 in the year studied
Intentional
  2 in the year studied
Unknown
  2 – both US Registered aircraft operated in foreign countries
Notes: Finally we had one pilot incapacitation accident, 2 intentional collisions with terrain (only one of which was fatal), and 2 accidents involving US registered aircraft operating abroad.
(Next Slide)

## Slide 10: Safety Risk Management (SRM) Solutions
Preflight Risk Assessments
  PAVE Checklist
  Flight Risk Assessment Tools (FRATs)
Maintain Situational Awareness
  In flight environmental assessments
    Weather, fuel, fatigue, etc.
Plan Continuation Bias (Get-there-itus)
  Have a Plan B and resort to it before an emergency
Notes: Safety risk management is all about knowing what you’re getting into and understanding what capabilities and resources you have that will ensure that each flight is completed safely. (Click)
SRM begins with a solid Preflight Risk Assessment. The assessment considers the Pilot, the Aircraft, the Environment within which the flight will take place, and External Pressures that may affect pilot judgement and performance. (Click)
There are various Flight Risk Assessment Tools or FRATs available to assist pilots in building their Risk Assessments. (Click)
Good preflight risk assessments mean you’ll have excellent Situational Awareness when you take off. The trick is to maintain that awareness until you’re tied down or in the hangar at your destination. Maintaining Situational Awareness means you’re constantly adjusting your assessments by answering questions such as:
Is the weather what I expected? Is my groundspeed as predicted? How long will it be till I get to the next checkpoint or to my destination? What will be my fuel status when I get there?
Harder to answer are questions such as:
Am I becoming fatigued? Can I continue with my flight as planned or is it time to adjust my expectations? Am I making my decisions solely on the safety of flight or am I feeling pressure to complete the flight as planned? (Click)
That brings us to Plan Continuation Bias. You may know it as Get-there-itus. Whatever you call it it’s real and every pilot must learn how to rationally deal with it. This deadly bias will tempt you to delay resorting to Plan B until you’ve already entered Instrument Meteorological Conditions while trying to maintain VFR. It’s also contributed to pilots overflying en route fueling opportunities and running short of fuel at the destination. We’ll discuss this in depth in an upcoming Topic of the month but for now – deal with Get-there-itus by having a Plan B and maybe even C and make the decision to go to it before an emergency is in progress.
(Next Slide)

## Slide 11: Safety Risk Management (SRM) Solutions
Fly the aircraft first!
  EA 401
  Flight crew focused on burned out light bulb
  Aircraft descended to ground on autopilot
    99 Fatalities
Be expert at dealing with distractions
Notes: On 29 December 1972 Eastern Airlines Flight 401, Lockheed L-1011, was scheduled to fly from JFK in New York to Miami International Airport in Florida.
3 flight crew and one non-revenue company employee were in the cockpit as the flight began the approach to Miami.
After extending the landing gear on final approach the first officer noticed the nose wheel down & locked light was not illuminated. The approach was aborted and the aircraft entered a 2,000 foot holding pattern west of the airport The crew engaged the autopilot while all 4 cockpit occupants engaged in trouble shooting the problem. When the autopilot was engaged it was inadvertently placed in Control Wheel Steering (CWS) mode. In this mode the airplane would maintain the attitude last commanded by the pilot. One of the pilots – most likely the Captain – bumped the control column as he turned to speak with the flight engineer. The airplane was placed in a shallow descent that was maintained all the way to the ground. Four professional aviators – any one of whom could have detected the descent – were so focused on a non-critical task that they failed to detect and arrest the descent.
Autopilots are great at reducing pilot workload. And – let’s face it – they fly more precisely than we do. But autopilots must be monitored because they will maintain heading and altitude right into the ground if that’s what you’ve tasked them to do. (Click)
Distracted pilots have flown aircraft into terrain without auto pilot assistance too. No matter what you’re dealing with you must fly the aircraft first. Make sure you’re always under control, properly configured, and in a safe flight environment.
(Next Slide)

## Slide 12: Technological Solutions
Moving Maps
Weather graphics
Enhanced & Synthetic Vision
FRAT Applications
Performance monitors
Notes: There are a host of technological programs, applications, and devices that can aid pilots in situational awareness and risk assessment. Moving maps with terrain overlays are common so there’s no excuse for not knowing how close you are to a collision. Flight planning tools can now integrate with charting programs, cockpit displays and weather imagery. FRAT applications make it easy to conduct pre and in-flight risk assessments and performance monitoring equipment keeps pilots apprised of their aircraft’s capability.
Pilots have access to more information than ever before and that has already contributed to a 20-year reduction in CFIT accidents. But all that information comes in many different forms so pilots must be thoroughly familiar with and proficient in device operation and information interpretation.
(Next Slide)

## Slide 13: Tips & Tricks
Get regular proficiency training
  Good coaching keeps you at the top of your game
Participate in Scenario-based training
  Holistic approach to training and proficiency
Notes: Successful professionals, no matter what their specialty, rely on coaching to keep them on top of their game. Pilots are no exception. Regular proficiency training with a Flight Instructor is the best investment you can make in safety and peace of mind.
There are a wealth of proficiency training programs available. Of course we recommend FAA WINGS Pilot Proficiency Training but, no matter what program or instructor you choose – please participate in scenario-based training. This holistic approach to proficiency looks at all aspects of safe flight from preflight planning to securing the aircraft at the end of the flight. Holistic training reinforces your skill at collectively managing all pilot processes and tasks in realistic scenarios.
(Next Slide)

## Slide 14: Tips & Tricks
Preview trips with simulation
  Great for new destinations and procedures
    But get some instruction for challenging environments
  Also good to stay sharp on local procedures
Works well as a solo activity
  But even better with a Flight Instructor
Notes: You can keep your skills sharp between flights by flying simulators or flight training devices. Many feature realistic graphics so you can get a look at unfamiliar destination environments. And you can practice instrument procedures before you have to fly them for real. But one caution here – simulation is not adequate preparation for flights to unfamiliar challenging if not hostile environments such as mountains, obstructed, short runways, and high density altitude environments. For those areas consult a Flight Instructor who is thoroughly familiar with the environment. (Click)
Simulation works well as a solo activity but it’s much better if you have a flight instructor managing the simulator and scenario while you do the flying.
(Next Slide)

## Slide 15: Tips & Tricks
Make use of moving map technology
  Make sure databases are up to date
  Make sure you’re looking at current weather
Give yourself some room!
  Leave some distance between you and the terrain, weather, or airspace you’re trying to avoid.
Notes: Moving map, enhanced, and synthetic vision technology is now available on installed equipment and hand held devices. Nothing has done more for situational awareness than this technology but you have to commit to keeping the databases up to date and you must confirm that you’re looking at the latest weather imagery. Also be aware that even the latest weather pictures are not real time so give a wide berth to any weather you’re trying to avoid.
And the availability of this technology has given rise to a paradox: Pilots are more situationally aware than ever before but CFIT and weather accidents still occur and Pilot Deviations continue to rise. Perhaps this is because pilots are more confident in their position so they fly closer to things they’re trying to avoid. Obviously the solution is to give yourself some breathing room. That means at least a mile from airspace and 2000 feet vertically from terrain you’re trying to avoid. Airspace and terrain don’t move much but weather is very dynamic so greater clearance distances will be required.
(Next Slide)

## Slide 16: Wire strikes are almost exclusively confined to agricultural operations.
True
False
Notes: Presentation Note: Ask the audience to answer this question. When they have answered; click to reveal the correct answers.
Now for a quick review:
Wire strikes are almost exclusively confined to agricultural operations. (Click)
False – many wire strikes do occur in agricultural operations but they occur in en route operations as well.
(Next Slide)

## Slide 17: CFIT accidents occur primarily at night.
True
False
Notes: Presentation Note: Ask the audience to answer this question. When they have answered; click to reveal the correct answers.
CFIT accidents occur primarily during night conditions. (Click)
False: The majority of CFIT accidents occur during the day
(Next Slide)

## Slide 18: Two thirds of CFIT accidents occur in IMC conditions.
True
False
Notes: Presentation Note: Ask the audience to answer this question. When they have answered; click to reveal the correct answers.
Two thirds of CFIT accidents occur in IMC conditions. (Click)
(False – CFIT accidents are almost evenly split between IMC and VMC conditions.
(Next Slide)

## Slide 19: The order of priority in performing pilot tasks is:
Communicate, aviate, navigate
Aviate, communicate, navigate
Aviate, navigate, communicate
Notes: Presentation Note: Ask the audience to answer this question. When they have answered; click to reveal the correct answers.
The order of priority in performing pilot tasks is: (Click)
C – Aviate, navigate, communicate. It’s true that all of these things happen at nearly the same time but your first priority is to fly the airplane, followed by navigating so as to avoid impacting terrain. Once you’ve got those under control, it’s time to communicate your intentions.
(Next Slide)

## Slide 20: Good practices to avoid CFIT accidents are:
Manage Distractions
Seek proficiency training
Give yourself some room
Use Flight Risk Assessment Tools
Fly at least 500 AGL to avoid wires
All of the above
Notes: Presentation Note: Ask the audience to answer this question. When they have answered; click to reveal the correct answers.
Good practices to avoid CFIT are: (Click)
All of the above.
(Next Slide)

## Slide 21: Questions?
Notes: Presentation Note: You may wish to provide your contact information and main FSDO phone number here. Modify with
Your information or leave blank.
(Next Slide)

## Slide 22: Proficiency and Peace of Mind
Fly regularly with your CFI
Perfect Practice
Document in WINGS
Notes: There’s nothing like the feeling you get when you know you’re playing your A game and in order to do that you need a good coach (Click)
So fly regularly with a CFI who will challenge you to review what you know, explore new horizons, and to always do your best. Of course you’ll have to dedicate time and money to your proficiency program but it’s well worth it for the peace of mind that comes with confidence. (Click)
Vince Lombardi, the famous football coach said, “Practice does not make perfect. Only perfect practice makes perfect.” For pilots that means flying with precision. On course, on altitude, on speed all the time. (Click)
And be sure to document your achievement in the Wings Proficiency Program. It’s a great way to stay on top of your game and keep you flight review current.
(Next Slide)

## Slide 23: Thank you for attending
You are vital members of our GA safety community
Notes: Your presence here shows that you are vital members of our General Aviation Safety Community. The high standards you keep and the examples you set are a great credit to you and to GA.
Thank you for attending.
(Next Slide)

## Slide 24: The National FAA Safety Team Presents
Topic of the Month November
Controlled Flight Into Terrain (CFIT)
<Audience>
<Presenter>
< >
Notes: (QMS File Number) Original Author: J. Steuernagle March 2017 POC: K. CloverAFS-920 Operations Lead Office 562-888-2020
Presentation Note: This is the title slide for Controlled Flight Into Terrain (CFIT)
Presentation notes (stage direction and presentation suggestions) will be preceded by a Bold header: the notes themselves will be in Italic fonts.
Program control instructions will be in bold fonts and look like this: (Click) for building information within a slide; or this: (Next Slide) for slide advance.
Some slides may contain background information that supports the concepts presented in the program.
Background information will always appear last and will be preceded by a bold Background: identification.
We have included a script of suggested dialog with each slide. Presenters may read the script or modify it to suit their own presentation style.
The production team hope you and your audience will enjoy the show. Break a leg!
(Next Slide)